## Slide 1
SIH26123 · EDGE-AI DISTRIBUTED FLEET COORDINATION
If the control room dies,
the aisle should not.
Three warehouse AMRs. No central dispatcher. Each robot broadcasts, auctions work, and yields locally — including when a human blocks the corridor.
Prototype · Hyderabad 3PL rack floor · measured vs stop-and-wait
Notes: Hook, 12 seconds. Do not start with algorithms. Ask: what happens when 40 AMRs share one aisle and the 5G controller dies? Pause. Then: today they freeze. Ours keep working because each robot is its own controller.

## Slide 2
SIH26123 · THE REAL PROBLEM · 2/12
Indian 3PL warehouses already have the failure mode.
Narrow aisles
1-wide rack corridors. Two AMRs cannot pass. A picker or carton blocks the only gap.
Central WMS / 5G
Every move waits on the cloud. Latency, cost, and a single outage stop the shift.
Mixed traffic
Humans, forklifts, robots. Obstacles are not in the map. They appear mid-pick.
Stop-and-wait
Both robots see a conflict and freeze. Deadlock. Picks do not leave the aisle.
Notes: Name a city: Hyderabad 3PL, or any Indian e-commerce DC. Judges care that this is a warehouse problem, not a robotics paper. Stress mixed humans + robots and patchy indoor radio.

## Slide 3
SIH26123 · THE GAP · 3/12
Two common answers both fail on a live floor.
Central reservation
A fleet computer locks cells for everyone. Fast on a whiteboard. Dead when the link dies. Judges will ask: does Robot A know Robot B through a scheduler?
Stop-and-wait
Safe and dumb. On a 1-wide aisle both freeze. Our baseline never finishes 6 jobs in 800 ticks.
Notes: Do not dunk on industry unfairly. Say: central control is the default because it is easier to code. That is why teams fake decentralization. We refused that shortcut.

## Slide 4
SIH26123 · CORE IDEA · 4/12
Every robot is a planner + a radio.
They negotiate like drivers at an unsignalized junction — not like clients of a control room.
1
Sense
Local range-2 obstacle + peer pose/path.
2
Broadcast
Direct peer packets. No scheduler in the middle.
3
Auction
Distance + battery + congestion + workload.
4
Yield
UBPA right-of-way. One steps into a turnout.
5
Replan
Live block → new path or RELEASE + re-auction.
Notes: The junction metaphor is the usefulness. Cars do not call a traffic-light server for every meter. Neither should AMRs in a rack aisle.

## Slide 5
SIH26123 · ARCHITECTURE · 5/12
The dashboard is a spectator. It never assigns work.
Robot 1 local planner
Robot 2 local planner
Robot 3 local planner
Peer broadcast · PEER_STATE / BID / YIELD_QUERY · not a dispatcher
Conflict from planned_path
Local negotiation
UBPA yield / replan
Judge question: does Robot A know what Robot B is doing directly, or through something else? Answer: directly, through the peer broadcast.
Notes: Point at the live radio panel during the demo. That packet feed is the proof. If they cannot see packets, it looks like a central brain with a pretty UI.

## Slide 6
SIH26123 · INNOVATION · 6/12
UBPA: an explainable right-of-way, not a token ring.
U
Urgency
Hot order / perishable pick scores higher.
B
Battery
Low battery should not sit in a deadlock.
P
Priority
Role / SLA weight, still local.
A
Arrival
Who reached the conflict first.
Notes: If scores tie or radio is stale: stalemate timeout, then lower robot_id yields. Deterministic. Never 'if robot_id == R1: pass'.

## Slide 7
SIH26123 · ALGORITHM · 7/12
Four local rules. Zero central locks.
Auction cost
distance + battery penalty + congestion + workload. Lowest valid bid wins. Invalid if battery cannot finish pick+drop.
Space-time A*
Each robot plans around peer paths it has heard. The world does not reserve cells for the fleet.
UBPA yield
On head-on: lower score steps into a turnout. Negotiation packets: YIELD_QUERY / ACK / NACK.
Stalemate
If both have stale data for 8 ticks, lower id yields. Then replan. If pick is unreachable, RELEASE and re-auction.
Notes: Keep this slide fast. Algorithm is backup for a technical judge. The live demo is the product.

## Slide 8
SIH26123 · INDIA VALIDATION · 8/12
Hyderabad 3PL rack map, not an empty grid.
Layout
25×11 cells. 1-wide rack aisles. Two highways. Depot and charger. Turnout bays so a yield is physically possible.
Traffic mix
Mouse click = human / forklift / fallen carton. Robots sense range 2, broadcast the obstacle, replan.
Radio reality
Indoor 5G/Wi-Fi is lossy: at 40% packet loss the same 6/6 still finish, just later (93–125 ticks vs 72 clean) with 0 deadlocks. Sliders are live.
Why here
Indian 3PLs buy AMRs faster than they buy a second control room. Edge negotiation is the cheap resilience.
Notes: If asked for a customer: any 3PL doing e-commerce pick-pack with AMRs. We did not fake a signed MoU. The map is a faithful aisle geometry, not a brand name.

## Slide 9
SIH26123 · MEASURED RESULTS · 9/12
Same map. Same seeds. Baseline never finishes.
Do not say “X% faster.” There is no finish time to divide. Source: results/metrics.json
Experiment
Stop-and-wait
UBPA
E1 throughput
incomplete · 0/6 jobs · 2 deadlocks
72 ticks · 6/6 · 0 deadlocks
E2 head-on aisle
incomplete · 1/3 jobs · 2 deadlocks
51 ticks · 3/3 · 0 deadlocks
E3 aisle blocked t=16
incomplete · 3/6 jobs · 3 deadlocks
85 ticks · 6/6 · 0 deadlocks
How to read this
Stop-and-wait freezes on mutual occupancy, so distance is low and wait ≈ 1. UBPA travels farther because it finishes the jobs. Tick limit 800. comparable=false, so improvement % is n/a.
Notes: Memorize: 72 / 51 / 85. Baseline deadlocks. Ours finishes. If they push for a percentage, repeat: a percentage against an incomplete baseline is a lie.

## Slide 10
SIH26123 · LIVE DEMO · 10/12
python scripts/run_demo.py → http://127.0.0.1:8765/
0:00
Three AMRs. No dispatcher. Point at the radio feed.
0:40
Auction: lowest valid cost. That is why a nearer robot took the pick.
1:10
Head-on in the 1-wide aisle. UBPA. One yields. Both continue.
1:50
BLOCK AISLE or click a cell. Replan or RELEASE + re-auction.
2:10
Drag packet-loss to 40%: same 6/6 finish, later (93–125 vs 72), 0 deadlocks.
2:25
Flip policy to stop-and-wait. Same map. They stall. That is the usefulness.
Notes: Practice twice with a timer. Have a 20-second backup screen recording if the judging laptop has no Python. Live first. Recording is insurance. Radio honesty if asked: 40% loss still completes 6/6 in 93-125 ticks with 0 deadlocks; 3 ticks of delay still never deadlocks but starves E1 to 3/6 with 577 intention conflicts; 70% loss lands only 1-5/6. All of that is results/degradation.json, measured, not typed.

## Slide 11
SIH26123 · DEPLOYMENT PATH · 11/12
Honest path. We did not fake a warehouse pilot.
1
Now
Laptop sim. Same robot code. Spectator dashboard.
2
Next
One Raspberry Pi per robot. UDP multicast = this PeerBus.
3
Pilot
3 AMRs, one aisle, one human picker, one blocked carton.
4
Scale
Only after the 3-robot yield works on hardware.
What we do not claim
Real AMRs, production 5G mesh, on-robot GPU, 40-robot scale, or a signed 3PL deployment. Simulated: radio, lidar-range sense, battery drain, laptop clock as edge CPU proxy.
Notes: Honesty here scores. Teams that claim a live warehouse with a grid sim get torn apart. Offer the Pi path as the next funded step.

## Slide 12
Robots that argue in the aisle
do not wait for a control room.
Who assigns tasks? Nobody. Each robot bids.
Who has right of way? UBPA, then robot id.
What if radio is stale? Stalemate timeout. Lower id yields.
python scripts/run_demo.py
Notes: Close on the line, then wait for questions. Do not keep talking. If they ask usefulness: a picker in the aisle is not an exception — it is the job. Central control treats humans as faults. This treats them as traffic.